| Vol. 18 | October 31, 2005 |
| --- | --- |
| Introduction The ATA-151/152 is a one-port telephone gateway with IP sharing function. There is no necessary to set up any extra device that the embedded NAT function can allow user PC to gallop on internet via ATA-151/152 directly. Further more users can take advantage of many new and exciting IP telephony applications by connecting analog phone to ATA-151/152. It is standard-based communication device that deliver true, next generation voice-over-IP (VoIP) application to residences and small-to medium enterprise in internet communication environment. More info... |
| Application diagram |
| Specification |
| Physical interface RJ-45 A. WAN X 1 for internet connection B. LAN X 1 for PC connection RJ-11 Phone X 1 for regular phone connection PSTN X 1 for connecting to fixed line (ATA-152 only) Power A. Voltage : DC 12 V B. Current : 1 A LED A. WAN: WAN link status indication B. LAN: LAN link status indication C. Status: VoIP status indication D. Power: Power status indication E. Phone: Analog phone status indication Dimension: 9.9 X 9.9 X 3.2 cm Protocol SIP RFC 3261 Outbound proxy Support IP or domain name for primary and secondary proxy address and auto switching is enabled. Nortel SIP-Ping supported Call function Call Forwarding Call Transfer Unconnection LED alarm Call Hold Call Waiting Calling Number Delivery Voice feature Voice codec G.711(A-law/μ-law) G.723.1 G.729 G.711 FAX pass-through mode RTP / RTCP Echo Cancellation G.168 Silence Detection/Suppression Comfort Noise Generation DTMF Detection/ Generation Call Tone Generation Network Network connection PPPoE (RFC 2516) a. Account / password can be saved b. Auto reconnection after disconnection DHCP client (for WAN port) Static IP DHCP Server and NAT Bridge for LAN interface QoS ToS Diff Serv Support SNTP System management Support Web, Telnet for remote control Username / Password for login to make configuration Firmware update / upgrading TFTP / FTP / Web remote update Environment AC Power 110~220V ± 10V 60Hz ± 3Hz Environment Temprature：0°C~40°C Hmidity：10％~90％RH Certification FCC Part 15, CE Class B, LVD |
| Welltech Computer Co., Ltd. TEL : +886-2-82265699 FAX : +886-2-82265799 http://www.welltech.com |